## Slide 1: PID controller

## Slide 2: What’s a PID controller?
A PID is defined by the following Equation
Think of the Integral term as the “past”
Think of the e(t) (proportional) term as “Now”
Think of the Derivative term as the “Future”
The constants reflect how important we think each of the other components are.

## Slide 3: In code: Setup
void setup()
{
…
for (int i = 0; i < REF_ANGLE_SAMPLES; i++){
getAccAngle();
getGyroValues();
maxGyro = absMax(gy,absMax(gx,gz));
maxAngle = absMax(theta,psi);
angle = compositeFilter( maxAngle, float(maxGyro), SAMPLE_RATE, angle);
refAngle += angle; delay(SAMPLE_RATE);
}
refAngle /= REF_ANGLE_SAMPLES;
…
}

## Slide 4: In code: Loop
void loop()
{
…
angle = compositeFilter( maxAngle, float(maxGyro), rate, angle);
float error = angle - refAngle;
integral = integral + error * rate;
derivative = (error - prevError) / rate;
spd = (KP * error) + (KI * integral) + (KD * derivative);
prevError = error;
…
}