## Slide 1: IMU and Servo Setup

## Slide 2: Wiring the IMU
The IMU Pins
  VCC (+5 Volts) -> VCC
  GND(Common) -> GND
  SDA -> D1
  SCL -> D0

## Slide 3: Accelerometer: What are we reading?
Acceleration due to gravity
We are intrested in:
  Theta
  Psi

## Slide 4: Small Angle Approximation
Small Angle Approximation good to

## Slide 5: Reading the Accelerometer
Use the FREE IMU library to get the raw Acceleration measurements out of the Accelerometer
Compute Theta and Psi

## Slide 6: Setup
void accBegin(){
Accel.init(ADXL345_ADDR_ALT_LOW); Accel.set_bw(ADXL345_BW_12);
}
void setup(){
accBegin();
Serial.begin(115200);
}

## Slide 7: Angle Calculation
void getAccAngle(){
float acc_data[3];
Accel.get_Gxyz(acc_data);
theta = (acc_data[0]/sqrt(acc_data[1]*acc_data[1] + acc_data[2]*acc_data[2]))*180/PI;
psi = (acc_data[1]/sqrt(acc_data[0]*acc_data[0] + acc_data[2]*acc_data[2]))*180/PI;
}
void loop() {
getAccAngle();
Serial.print(millis());
Serial.print(" , ");
Serial.print(theta);
Serial.print(" , ");
Serial.println(psi);
}

## Slide 8: Sample Data
Chart: Time (Seconds)